## Slide 1: SPARE PARTS INVENTORY MANAGEMENT
Project Group Members:
Mahdi Attieh
Haneen Saymeh Hisham Jaber Aya Abuzant
Supervised by:
Dr. Yahya Saleh
An – Najah National University
Faculty of Engineering Industrial Engineering Department

## Slide 2
Agenda
Introduction
Inventory Management
Spare Parts
Spare Parts Management
Literature Review
Problem Statement
Proposed Solution
Methodology
ABC Classification
Demand Forecasting
Inventory Management Models
Model Formation
Results & Discussion
Conclusions
Recommendations
Limitations
Inventory Costs
Notes: <number>

## Slide 3
Introduction

## Slide 4
Introduction – Inventory Types
Materials and components scheduled for use in making a product.
WIP: materials and components that have begun their transformation to finished goods.
Goods ready for sale to customers.
Returned goods that are salable.
Replicable Parts
Notes: <number>

## Slide 5
Inventory Management
It is primarily concerned about specifying the size and placement of stocked goods. Inventory management is required at different locations within a facility or within multiple locations of a supply chain network to protect the regular and planned course of production against the random disturbance of running out of materials or goods.
Notes: <number>

## Slide 6
Spare Parts
This category includes those products, which are complimentary to the main
products produced for the purpose of sale.
Spare parts are kept in stock to support maintenance operations and to protect equipment failures.
Although this function is well understood by maintenance managers, many companies face the challenge of keeping in stock large inventories of spares with excessive associated holding and obsolescence costs.
Thus, effective cost analysis can be an important tool to evaluate the effects of stock control decisions related to spare parts.
Notes: To protect against equipment failures … Do you mean ’protect equipment failures’ ?? I already changed it
<number>

## Slide 7
Spare Parts Management
Service parts management is the main component of a complete Strategic Service Management process that companies use to ensure that right spare parts and resources are at the right place (where the broken part is) at the right time.
It plays an important role in achieving the desired plant
availability at an optimum cost.
Presently, industries use capital intensive, mass
production oriented and sophisticated technology.
The downtime for such plant and machinery is
prohibitively expensive.
Notes: <number>

## Slide 8
Literature Review

## Slide 9: Literature Review
Most studies began in the last decade on the spare parts inventory management.
Although theoretical models for slow-moving items are abundant in inventory literature since 1965.
Most of these studies in spare parts literature are focused on testing forecasting methods for demand of slow-moving items rather than on implementing inventory models.

## Slide 10: Literature Review (Partial List)
<number>
Research | Author | Date | About
(S - 1, S) model | Feeney and Sherbrooke | 1966 | A particular case of (s , S) models, with an underlying Poisson demand distribution. It’s well studied and suitable for slow-moving items, this type of policy requires continuous review of the inventory system. Moreover, the Poisson distribution assumes randomness of demand
Compound-Poisson models | Williams et al , Silver et al | 1971, 1984 | This distribution needs no information of demand other than the average demand, which is the sole parameter of the demand distribution. However, these models are more difficult to apply in practice because they need an assumption on the compounding distribution.

## Slide 11: Literature Review (cont…)
<number>
Research | Author | Date | About
Inventory models to control slow and fast moving items. | Gelders and van Looy | 1978 | Which were clustered in classes using ABC analysis together with criticality and value considerations.
Forecasting methods for the management of spare parts . | Ghobbar and Friend | 2003 | They present a comparative study of 13 different forecasting methods for the management of spare parts in the aviation industry. (No inventory models are included)
Bootstrap method to forecast intermittent demand of service parts. | Willemain | 2004 | They used it to forecast intermittent demand of service parts, and they implement the method on a large industrial data set. (Also no inventory models are included)

## Slide 12
Problem Statement
&
Solution

## Slide 13: Problem Statement
In this Project we present a case study in inventory management of spare parts at Al Sarawi for Mercedes Spare Parts; a local Palestinian company.
The company’s core business is selling spare parts for Mercedes Cars to consumers. The company does not give adequate importance to inventory management.
As a result, there is an inefficient deployment of inventory.
This study focuses on the inventory management of spare parts for a specific model of Mercedes Cars which is 416.
It is important for the company has a well-planned inventory management process for spare parts to control cost and service customer needs.

## Slide 14: Proposed Solution
We need to minimize the total costs of the inventory in the company through developing and optimizing various inventory management models of the company’s various spare parts
1. Building Inventory Models and Ordering Policy for the spare parts being considered in our study
2. Conducting a trade-off analysis via comparing the characteristics of the current and the new inventory models at the company

## Slide 15
Methodology

## Slide 16
Methodology
Determine and classify the spare part items by using ABC analysis.
Forecast the demand by analyzing the historical sales data available.
Collect Relevant Cost Data ( Holding Cost , Ordering Cost, Transportation cost, Backordering cost ).
Build Inventory Models for each category of the classified spare parts ( A , B , C ).
Evaluate the previous conditions and compare them
empirically with the new results based on our
inventory models.
Notes: <number>

## Slide 17
ABC classification

## Slide 18
ABC Inventory Classification
The Italian economist Pareto (1848-1923) observed in 19th century that 20% of the population owned 80% of the usable land (Pareto 1935).
Pareto found the same distribution in other economical and natural processes.
Notes: <number>

## Slide 19
ABC Classification … Cont.
(A) Category items: these are the 20% of the items that tie up to 80%
of the total inventory money
(B) Category items: these are the 30% of the items the tie up to 15% of
the total inventory money
(C) Category items: these are 50% of the items that tie up to 5% of the
total inventory money
Notes: <number>

## Slide 20: Cont….
Sample of A items
Sample of B items
Sample of C items

## Slide 21: Cont…

## Slide 22: Cont..

## Slide 23
Demand Forecasting

## Slide 24
Demand Forecasting
It is often the first critical step in any planning activity especially inventory planning.
It’s purpose is to determine the required quantity of parts that need to be ordered.
This project analyzes 2 years data of demand divided in to 4 intervals for each 6 months, for 85 items
Notes: <number>

## Slide 25: Forecasting Methods
Naïve Approach
Moving Averages
A simple moving average
A weighted moving average
Exponential Smoothing

## Slide 26: Simple moving average
Sample of A items
Sample of B items
# | ID | ABC | D 1-6\2010 | D 6-12\2010 | D 1-6\2011 | D 6-12\2011 | D forcast1-6\2011 | D forecast 6-12\2011 | D forecast 1-6\2012
1 | 25200012 | A | 40 | 30 | 30 | 20 | 35 | 30 | 25
2 | FNS00007 | A | 65 | 120 | 120 | 90 | 93 | 120 | 105
# | ID | ABC | D 1-6\2010 | D 6-12\2010 | D 1-6\2011 | D 6-12\2011 | D F 1-6\2011 | D F 6-12\2011 | D F 1-6\2012
1 | S0011097 | B | 3 | 7 | 5 | 6 | 5 | 6 | 6
2 | 25000024 | B | 9 | 7 | 10 | 18 | 8 | 9 | 14

## Slide 27: A weighted moving average
Sample of A items
Sample of B items
# | ID | ABC | D 1-6\2010 | D 6-12\2010 | D 1-6\2011 | D 6-12\2011 | Forecast D1-6\2011 | Forecast D 6-12\2011 | Forecast D 1-6\2012
1 | 25200012 | A | 40 | 30 | 30 | 20 | 34 | 30 | 24
2 | FNS00007 | A | 65 | 120 | 120 | 90 | 98 | 120 | 102
# | ID | ABC | D 1-6\2010 | D 6-12\2010 | D 1-6\2011 | D 6-12\2011 | Forecast D1-6\2011 | Forecast D 6-12\2011 | Forecast D 1-6\2012
1 | S0011097 | B | 3 | 7 | 5 | 6 | 6 | 6 | 6
2 | 25000024 | B | 9 | 7 | 10 | 18 | 8 | 9 | 15

## Slide 28: Criteria for choosing time series methods
Mean absolute deviation (MAD)
Mean absolute percent error (MAPE)

## Slide 29: Forecasting error for moving average method
Sample of A items
Sample of B items
Sample of C items
# | ID | ABC | error1-6\2010 | error6-12\2010 | error1-6\2011 | error6-12\2011 | Sum Error | MAD avg | MAPE
1 | 25200012 | A | 0.00 | 0.00 | -5.00 | -10.00 | 15.00 | 3.75 | 16.67
2 | FNS00007 | A | 0.00 | 0.00 | 27.00 | -30.00 | 57.00 | 14.25 | 13.96
# | ID | ABC | error1-6\2010 | error6-12\2010 | error1-6\2011 | error6-12\2011 | Sum Error | MAD avg | MAPE
1 | S0011097 | B | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
2 | 25000024 | B | 0.00 | 0.00 | 2.00 | 9.00 | 11.00 | 2.75 | 17.50
# | ID | ABC | error1-6\2010 | error6-12\2010 | error1-6\2011 | error6-12\2011 | Sum Error | MAD avg | MAPE
1 | 99800001 | C | 0.00 | 0.00 | 0.00 | 5.00 | 5.00 | 1.25 | 6.58
2 | F0007517 | C | 0.00 | 0.00 | 9.00 | 0.00 | 9.00 | 2.25 | 18.75

## Slide 30: Forecasting error for weighted average method
Sample of A items
Sample of B items
Sample of C items
# | ID | ABC | Error1-6\2010 | Error6-12\2010 | Error1-6\2011 | Error6-12\2011 | sum error | MAD W.Avg | MAPE
1 | 25200012 | A | 0.00 | 0.00 | -4.00 | -10.00 | 14.00 | 3.50 | 15.83
2 | FNS00007 | A | 0.00 | 0.00 | 22.00 | -30.00 | 52.00 | 13.00 | 12.92
# | ID | ABC | Error1-6\2010 | Error6-12\2010 | Error1-6\2011 | Error6-12\2011 | sum error | MAD W.Avg | MAPE
1 | S0011097 | B | 0.00 | 0.00 | -1.00 | 0.00 | 1.00 | 0.25 | 5.00
2 | 25000024 | B | 0.00 | 0.00 | 2.00 | 9.00 | 11.00 | 2.75 | 17.50
# | ID | ABC | Error1-6\2010 | Error6-12\2010 | Error1-6\2011 | Error6-12\2011 | sum error | MAD W.Avg | MAPE
1 | 99800001 | C | 0.00 | 0.00 | 0.00 | 5.00 | 5.00 | 1.25 | 6.58
2 | F0007517 | C | 0.00 | 0.00 | 9.00 | -1.00 | 10.00 | 2.50 | 21.88

## Slide 31: Forecasting accuracy for demand
E:ExponentiaSmoothing Method
W: Weighted moving average
A: simple average method N: Naïve Method
Item Classes | Best Forecasting Method | Accuracy Measures | Forecasting Method Accuracy | Percentage of the total items
A items 17 items | Weighted moving average and simple average method | MAD MAPE | E: 3 items A: 11 items W: 15 items N: 0 items | E:17.6% A:29.4% W:64.7% N: 0%
B items 21 items | Weighted moving average and simple average method. | MAD MAPE | E: 2 items A: 13 items W: 15 items N: 0 items | E:9.5% A:61.9% W:71.4% N: 0%
C items 45 items | Weighted moving average and simple average method. | MAD MAPE | E: 10 items A: 26 items W: 32 items N: 0 items | E: 22.2% A:57.7% W:71.1% N: 0%
Total Items 85 items |  |  |  | 

## Slide 32
Inventory Cost

## Slide 33: Inventory Costs
Calculating cost of holding inventory and ordering cost and the measurement of various management practices.
Inventory cost is generally regarded by the company in terms of annual cost.
The general elements that make up the cost of holding inventory can be classified as non capital and capital. This cost is an annual estimate and should be carefully identified.
<number>

## Slide 34
Inventory Costs - Cost of holding items in the inventory
It comprises the cost of equity and after-tax cost of debt.
WACC is not calculated in this study, because Sarrawi Company is not an equity company and it doesn’t have debt, it’s a family business owned by Al Sarrawi family.
‘The opportunity cost of all capital invested in an enterprise’ .
Notes: <number>

## Slide 35
Inventory Costs - Cost of holding items in the inventory
Warehousing rental
Transportation
Obsolescence
Pilferage/theft
It varies from business to business.
Generally non-capital cost is identified as:
In this case study, the non capital costs are:
Logistics costs
Tax and utility human resource for the warehouse.
Administrative and human resource for the warehouse
Damage
Insurance
Tax and duty
Administration cost (accounting, management)
Notes: <number>

## Slide 36: Cont..
The costs of logistics were obtained by the cost of every shipments contains 6-10 pallets every order ,so we conclude in average the total cost of logistics is 1600 N.I.S every order.
Taxes and rental of human resource for warehouse also were taken.
Administrative and human resources were used to calculate the non capital costs.

## Slide 37: Cont…
Total Inventory Holding Cost: Combining non-capital and capital costs gives the total inventory holding cost. Non-capital costs are stated on before-tax basis.
Logistics | Admin | Taxes | Total Non Capital Cost | Total Capital Cost | Avg Aggregate Inventory Value | Holding Cost
1,600 | 210,000 | 18,500 | 230,100 | 0 | 800,000 | 29%

## Slide 38
Inventory Management Models

## Slide 39: Inventory Management Models
Good management of inventory is required to manage the supply of product, its spares or consumables and satisfy the customer’s needs.
So we sought to make a balance between meeting the customer’s demands and requirements at a minimum cost to the suppliers.
<number>

## Slide 40: Inventory Management Models
There are two basic types of inventory system that we used:
I. Continuous review
II. Periodic review
In our project we will be using the continuous and the periodic review systems on the A B and C items to insure that we find the most optimal feasible solution.
<number>

## Slide 41
Model Formation
Find he Optimal Ordering Quantity : The EOQ formula was
used to determine the optimal Q to be ordered.
Where:
Q = order quantity
EOQ = optimal order quantity
D = annual demand quantity
S = fixed cost per order
H = annual holding cost per unit
Notes: <number>

## Slide 42: Model Formation for EOQ
Sample of A items
Sample of B items
Sample of C items
# | ID | ABC | Unit Value | D Forecasted multiplied by 2 | EOQ 2012 | Q Current | Safety Stock | Setup Cost
1 | 25200012 | A | 180.00 | 48 | 55 | 100 | 10 | 1600
2 | FNS00007 | A | 65.00 | 204 | 187 | 200 | 20 | 1600
# | ID | ABC | Unit Value | D Forecasted multiplied by 2 | EOQ 2012 | Q Current | Safety Stock | Setup Cost
1 | S0011097 | B | 600.00 | 12 | 15 | 10 | 2 | 1600
2 | 25000024 | B | 320.00 | 12 | 21 | 5 | 5 | 1600
# | ID | ABC | Unit Value | D Forecasted multiplied by 2 | EOQ 2012 | Q Current | Safety Stock | Setup Cost
1 | 99800001 | C | 45.00 | 34 | 92 | 60 | 15 | 1600
2 | F0007517 | C | 240.00 | 20 | 31 | 30 | 5 | 1600

## Slide 43
Model Formation - Continuous Review System
Reorder point = Average demand during lead time + Safety Stock.
Choosing an Appropriate Service -Level Policy (z)
Finding the Safety Stock, assuming the demand is normally distributed
Where:
σt= standard deviation of daily demand.
L = Lead time.
Notes: <number>

## Slide 44
Model Formation – Periodic Review System
1. Reorder point = Average demand during lead time and the protection period + Safety Stock.
Where: P = Protection period , L= Lead time.
2. Finding the Safety Stock
Where:
σt= standard deviation of daily demand.
σp+L= Standard deviation for daily demand + Protection time
3. Time Between Order (TBO) =
Notes: <number>

## Slide 45: Model Formation…cont
Calculating the total costs for the new ordering quantity and current one for the two systems.
Total Cost = Annual holding cost + Setup Cost + Safety stock holding cost.
Where
C = Total cost per year.
Q = Lot size, in units for the new and current quantity.
H = cost of holding one unit is inventory for a year.
D = Annual demand, in units per year.
S = Cost of ordering or setting up one lot.
<number>

## Slide 46: Model Formation…cont
Daily demand, Service level, and the lead time for A items
<number>
# | ID | ABC | Lead time(L) | Average daily demand | z (service level) | d.L | σL
1 | 25200012 | A | 3 | 0.160 | 1.65 | 0.480 | 0.094
2 | FNS00007 | A | 3 | 0.680 | 1.65 | 2.040 | 0.307
Sample of A items
# | ID | ABC | Lead time(L) | Average daily demand | z (service level) | d.L | σL
1 | S0011097 | B | 3 | 0.040 | 1.65 | 0.120 | 0.020
2 | 25000024 | B | 3 | 0.040 | 1.65 | 0.120 | 0.056
Sample of B items

## Slide 47: Model Formation
Continuous Review System for a sample of A and B items
<number>
# | ID | ABC | Safety stock | Reorder point | Q new | Q/2 * H | D/Q * S | Cost New | SS current | Q current | D/Q*S Current | Q/2* H Current | Cost Current
1 | 25200012 | A | 1 | 2 | 55 | 1436 | 1396 | 2884 | 10 | 100 | 768 | 2610 | 3900
2 | FNS00007 | A | 1 | 4 | 187 | 1762 | 1745 | 3527 | 20 | 200 | 1632 | 1885 | 3894
3 | F0015261 | A | 1 | 2 | 15 | 1958 | 1920 | 4139 | 2 | 5 | 5760 | 652.5 | 6934.5
4 | 7000072 | A | 1 | 3 | 49 | 4263 | 4114 | 8551 | 20 | 20 | 10080 | 1740 | 15300
# | ID | ABC | Safety stock | Reorder point | Q new | Q/2 * H | D/Q * S | Cost New | SS current | Q current | D/Q*S Current | Q/2* H Current | Cost Current
1 | S0011097 | B | 1 | 2 | 15 | 1305 | 1280 | 2759 | 2 | 10 | 1920 | 870 | 3138
2 | 25000024 | B | 1 | 2 | 21 | 974 | 914 | 1981 | 5 | 5 | 3840 | 232 | 4536

## Slide 48: Model Formation
<number>
Periodic Review System for a sample of first 5 C items
# | ID | ABC | l | d | z | p (TBO) | бp+l | SS | Target Inventory | Current SS | Q/2 * H | D/Q * S | Cost New
1 | 99800001 | C | 3 | 0.113 | 1.65 | 811.765 | 8.605 | 15 | 108 | 15 | 600 | 591 | 1387
2 | F0007517 | C | 3 | 0.067 | 1.65 | 465.000 | 2.129 | 4 | 36 | 5 | 1079 | 1032 | 2389
3 | 72700017 | C | 3 | 0.087 | 1.65 | 403.846 | 2.253 | 4 | 40 | 2 | 1218 | 1189 | 2685
4 | 76000050 | C | 3 | 0.680 | 1.65 | 520.588 | 26.866 | 45 | 402 | 30 | 924 | 922 | 2081
5 | 72700021 | C | 3 | 0.300 | 1.65 | 606.667 | 14.845 | 25 | 208 | 20 | 792 | 791 | 1800

## Slide 49
Results
& Discussion

## Slide 50: Results and Discussion – Class A
The results clearly show that the chosen continuous review system
model has marked improvement over the existing method.
The inventory cost savings are 97,640 NIS with percentage of 12.21 %.
It also shows how the periodic review system is saving money for the A
items but it is not applicable in this company due to the high amount of
inventory and the long period to restock.
 | Old current | New Inventory model (Continuous Review System) | New inventory model (Periodic Review System)
Total Parts | 17 | 17 | 17
Inventory cost per year, NIS | 180,978 | 83,284 | 84,963
Percentage improvement | “_” | 12.21% | 12%

## Slide 51: Results and Discussion – Class B
The inventory cost savings for the continuous review system are 36,559
NIS with percentage 4.57 % .
It also shows a similar savings for the periodic review system with
percentage of 3.05 % . (as mentioned previously the long periods between ordering ordering make is not applicable in this company).
 | Current model | New inventory model (Continuous Review System) | New inventory model (Periodic Review System)
Total Parts | 22 | 22 | 22
Inventory cost per year, NIS | 88,631 | 52,072 | 64,227
Percentage improvement | “_” | 4.57% | 3.05%

## Slide 52: Results and Discussion Results for class C
The inventory cost savings are 68,445 NIS with percentage of 8.56 %.
Using the periodic review system saves even more with a percentage of
9.96 % but this system is not applicable in this company due to the long periods between ordering, even if the periodic system is preferred for the C items but 1 or 2 years the time between orders make it infeasible.
 | Current model | New inventory model (Continuous Review System) | New inventory model (Periodic Review System)
Total Parts | 46 | 46 | 46
Inventory cost per year, NIS | 132,327 | 63,882 | 52,637
Percentage improvement | “_” | 8.56% | 9.96%

## Slide 53: Results

## Slide 54: Results

## Slide 55
Conclusion
&
Recommendation

## Slide 56: Conclusion
Spare parts supply chains are in fact very different from those of finished goods supply chain. The fundamental driving forces are balancing between having a low inventory of spare parts to decrease the cost and service fulfillment with short response time.
The company in this study lacks of expertise in the area of inventory management. This has resulted in severe shortcomings in the business process of their company. After reviewing and analyzing the data collected we proposed a cost effective solution for them to manage their inventory optimally.
By implementing an effective inventory management system, Al-Sarrawi Company in this study will be able to save a lot of money and keeping their services as it is to their customers.

## Slide 57: Conclusion…cont.
By implementing an effective inventory management system, Al-Sarrawi Company in this study will be able to save a lot of money and keeping their services as it is to their customers.

## Slide 58: Recommendation
Applying the inventory model successfully depends on the effective implementation of every stage of the framework of inventory management which includes ABC analysis, demand forecasting and implementation development of an inventory model.
Inaccurate data going into a perfect model will give inaccurate or even misleading results. Perfect data going into an unsuitable model similarly will give inaccurate results.

## Slide 59: Limitations
The limitation in this project has been the amount of data available. Clearly the data obtained does not cover a long enough time-frame to provide accurate forecast so in a more few years of stored data will give better results and accurate assumptions, and the system needs to be continually updated or it will become invalid.

## Slide 60
Any Questions